## Slide 1: Simulated Control of a 3DoF Mobile Robot Arm
Nathan Park

## Slide 2: Goals
Set up simulation based on 3DoF example
Implement 3 massless links to allow movement of the base
Implement PID control to track goal state
Input arbitrary path waypoints and test tracking

## Slide 3: Mobile Robot Implementation
Add 3 massless DoFs for base motion in X, Y, Z direction
  Extend syms code and Simulink model to accommodate 6 degrees of freedom
  Use prismatic joints for new massless joints
  Test it!

## Slide 4: Oops.

## Slide 5: Floor Collision!
Tried two approaches:
  Clamp position to > 0
  Flip velocity sign when pos < 0
Simulink doesn’t like the discontinuous behavior, and this doesn’t represent the physical phenomenon
Spring + Damper implementation
  Good model of the dynamics of ground collision/bouncing
  Need a really stiff spring constant
  Played with values until it looked good

## Slide 6: Fixed!

## Slide 7: PID Implementation
Need to tell the robot where to go
Use Simulink PID block to implement
Calculate error of current position to goal position
Break out P, I, D, N constants into 6x1 vectors for tweaking individual DoFs

## Slide 8: PID Implementation
Not particularly experienced with PID control
Just played with the values
  Improved prediction with larger D constant
  Error correction over time improved with larger I constant
  P increased “stiffness” causing lots of jerky movements

## Slide 9: Path Generation from Waypoints
Simple code
  Clock input for time varying function
  Takes in 5 waypoints
  Each waypoint traveled to over 2 sec (10 sec sim / 5 positions)
  Polyfit to generate a fit for each theta

## Slide 10: Path Generation from Waypoints

## Slide 11: Tracking Analysis
Low PID constant values struggle to overcome gravity
Hard to tune because of the system complexity, mostly a guessing game

## Slide 12: Tracking Analysis
Z-direction force starts very high due to the IC being away from the initial goal
Floor collision force is very large from initial drop and final drop

## Slide 13: Improvements
Improve PID tuning
Extend path generation capabilities
Create IK solution
  Add floor collision to links
  PID control of XYZ position rather than joint angles
Robot self collision?
More links on arm?